## Slide 1: Agenda
This slide is used as a ‘Template' for generating agenda slides. Please do not delete this slide.
Adjust the design of this slide and click the 'Sync Agenda' (in Agenda Lab) to replicate the design in the other slides.
Notes: This notes page is used to store data - Do not edit the notes. UFBUVGVtcGxhdGVNYXJrZXI=@VGl0bGUgMQ==@UHB0TGFic0FnZW5kYV8mXkBWaXN1YWxBZ2VuZGFJbWFnZV8mXkBNb3RpdmF0aW9uXzI=@UHB0TGFic0FnZW5kYV8mXkBWaXN1YWxBZ2VuZGFJbWFnZV8mXkBQcm9qZWN0IFNwZWNpZmljYXRpb25fMw==@UHB0TGFic0FnZW5kYV8mXkBWaXN1YWxBZ2VuZGFJbWFnZV8mXkBIaWdoIExldmVsIERlc2lnbl80@UHB0TGFic0FnZW5kYV8mXkBWaXN1YWxBZ2VuZGFJbWFnZV8mXkBJbXBsZW1lbnRhdGlvbiBhbmQgVGVzdGluZ181@UHB0TGFic0FnZW5kYV8mXkBWaXN1YWxBZ2VuZGFJbWFnZV8mXkBEZW1vXzY=@UHB0TGFic0FnZW5kYV8mXkBWaXN1YWxBZ2VuZGFJbWFnZV8mXkBFdmFsdWF0aW9uIGFuZCBDb25jbHVzaW9uXzc=@2188161514

## Slide 2: Distributed Road Traffic Speed Monitoring
Jeremy Chan
w/ Dr. Ed Stott
w/ Dr. Christos Papavassiliou
An EE4-T Final Year Project
Notes: Good morning.
My name is Jeremy Chan, and welcome to my final year project presentation, on creating a distributed road traffic speed monitoring system.

## Slide 3: At a glance…
Implementation based project
Catch speeding motorists using a camera and Raspberry Pi
Existing license plate recognition (LPR) technologies
New peer to peer network (P2P)
No government controlled central server
Social posting
Notes: At a glance, this project is an implementation based project.
It uses a camera connected to a Raspberry Pi to catch speeding motorists by detecting their license plates, sharing it with others, and working out the average speed of the vehicle.
Details of speeding motorists can then be posted online on social platforms.
It leverages existing LPR technologies, but creates a NEW P2P network, eliminating the need for a central, government controlled, server
The rundown on this presentation is a general overview on the project details, followed by high level design of the individual components, followed by implementation and testing.
Finally, a demo, followed by an evaluation and a conclusion.

## Slide 4
Agenda
Motivation / Project Specification / High Level Design /
Implementation and Testing / Demo / Evaluation and Conclusion

## Slide 6: Motivation
Chart: Casualties by severity and road type (2015)
| Fatal | Serious | Slight | All
Built Up | 43 | 67 | 73 | 72
Non Built Up | 51 | 30 | 22 | 23
Motorway | 6 | 3 | 5 | 5
Majority of accidents not on motorway
Target residential areas
73%
72%
67%
43%
23%
22%
30%
51%
Built up
Non built up
Motorway
https://www.gov.uk/government/uploads/system/uploads/attachment_data/file/533293/rrcgb-main-results-2015.pdf
Notes: The main motivation of the project comes from reducing casualties from speeding cars.
While the higher the speed, the higher the fatality rate, most of the casualties lie in residential and urban areas.
Therefore, the system is targeted at providing average speed checks across non-motorway areas.

## Slide 7: Motivation
Detrimental to streetscape
Discreet appearance
https://a1.muscache.com/locations/uploads/photo/image/22901/0_4200_0_2800_one_westside-los-angeles-quiet-residential-street-devon0289.jpg
Notes: Regular average speed check cameras in all their yellow and orange glory are horrible to look at.
Putting a lot of them near homes would be detrimental to the streetscape, and therefore a discreet implementation is desired.

## Slide 8: Related Work
https://www.bhphotovideo.com/images/images1000x1000/bosch_f_01u_245_613_dinion_capture_5000_license_1163861.jpg
https://ichef-1.bbci.co.uk/news/660/cpsprodpb/0202/production/_89841500_033220635-2.jpg
Require dedicated camera hardware
>£ 1000
Uses centralised server to store plates
Notes: There are some license plate cameras on the market with different features like enhanced night time operation with superior digital signal processing.
However they are rather expensive and always use a central server to store the detected license plates.

## Slide 10
Agenda

## Slide 12: Product Specification - Main Deliverables
Implement a UK number plate recognition system using existing computer vision algorithms on a low-cost, readily available hardware platform.
Set up a peer-to-peer network to share vehicle passing times and detect violations without the need for a central server.
Publish photo evidence of any violations
(Advanced deliverables in evaluation)
Notes: Therefore, the main deliverables of the project were formulated as follows:
The system should leverage existing computer vision algorithms to provide license plate recognition capabilities
For sake of simplicity, no custom plates, and only UK format
A peer to peer network should be created to share the detected plates with no need for a central server
The license plates should be able to be published online for further police action

## Slide 13: Product Specification - Main Deliverables
Implement a UK number plate recognition system using existing computer vision algorithms on a low-cost, readily available hardware platform.
Set up a peer-to-peer network to share vehicle passing times and detect violations without the need for a central server.
Publish photo evidence of any violations
(Advanced deliverables in evaluation)
Notes: Therefore, the main deliverables of the project were formulated as follows:
The system should leverage existing computer vision algorithms to provide license plate recognition capabilities
For sake of simplicity, no custom plates, and only UK format
A peer to peer network should be created to share the detected plates with no need for a central server
The license plates should be able to be published online for further police action

## Slide 14: Product Specification - Main Deliverables
Implement a UK number plate recognition system using existing computer vision algorithms on a low-cost, readily available hardware platform.
Set up a peer-to-peer network to share vehicle passing times and detect violations without the need for a central server.
Publish photo evidence of any violations
(Advanced deliverables in evaluation)
Notes: Therefore, the main deliverables of the project were formulated as follows:
The system should leverage existing computer vision algorithms to provide license plate recognition capabilities
For sake of simplicity, no custom plates, and only UK format
A peer to peer network should be created to share the detected plates with no need for a central server
The license plates should be able to be published online for further police action

## Slide 15: Product Specification - Main Deliverables
Implement a UK number plate recognition system using existing computer vision algorithms on a low-cost, readily available hardware platform.
Set up a peer-to-peer network to share vehicle passing times and detect violations without the need for a central server.
Publish photo evidence of any violations
(Advanced deliverables in evaluation)
Notes: Therefore, the main deliverables of the project were formulated as follows:
The system should leverage existing computer vision algorithms to provide license plate recognition capabilities
For sake of simplicity, no custom plates, and only UK format
A peer to peer network should be created to share the detected plates with no need for a central server
The license plates should be able to be published online for further police action

## Slide 16: Product Specification - Advanced Deliverables
Use the changes in the number plate geometry as the vehicle passes to detect the instantaneous speed of a vehicle
Implement automatic peer discovery
Add an encryption layer
Package the system so that it can be easily installed in a home by an inexperienced user.

## Slide 17: Product Specification - Advanced Deliverables
Use the changes in the number plate geometry as the vehicle passes to detect the instantaneous speed of a vehicle
Implement automatic peer discovery
Add an encryption layer
Package the system so that it can be easily installed in a home by an inexperienced user.

## Slide 18: Product Specification - Advanced Deliverables
Use the changes in the number plate geometry as the vehicle passes to detect the instantaneous speed of a vehicle
Implement automatic peer discovery
Add an encryption layer
Package the system so that it can be easily installed in a home by an inexperienced user.

## Slide 19: Product Specification - Advanced Deliverables
Use the changes in the number plate geometry as the vehicle passes to detect the instantaneous speed of a vehicle
Implement automatic peer discovery
Add an encryption layer
Package the system so that it can be easily installed in a home by an inexperienced user.

## Slide 21
Agenda

## Slide 23: High Level Design
3 well defined modules
Readily available components
Users have control over data
License Plate Detection
Peer to Peer Network
Web Interface

## Slide 24: Envisioned System
9:41 pm
9:41 pm
9:41 pm
9:44 pm
9:44 pm
9:44 pm

## Slide 26
Agenda

## Slide 28: License Plate Recognition - Aim
Get license plates of cars
Function in multiple angles and lighting conditions

## Slide 29: License Plate Recognition - Design
Store videos locally using motion detection
Detect license plates using OpenALPR
Extract unique plates
Multiple parameters for tweaking
Store plates with metadata in database
Consecutive frames will likely be the same car
Process videos when idle
  Time
  Location
Can survive power outages
Can survive busy periods

## Slide 30: License Plate Recognition - Fuzzy Grouping
Robust separation of unique vehicles
Sort by confidence
Works with misreads
LG65FBO --- LG65FBP --- LG65FBO --- FE16RBX --- LTZ1077 --- LTZ077 --- LTZ107
Plate1 | Plate 2 | String Similarity
LG65FBO | LG65FBP | 0.857
LG65FBO | FE16RBX | 0.285
LG65FBO | LTZ1077 | 0.143
FE16RBX | LTZ1077 | 0.143
LTZ1077 | LTZ107 | 0.923

## Slide 31: License Plate Recognition - Fuzzy Grouping
Robust separation of unique vehicles
Sort by confidence
Works with misreads
LG65FBO --- LG65FBP --- LG65FBO --- FE16RBX --- LTZ1077 --- LTZ077 --- LTZ107
Plate1 | Plate 2 | String Similarity
LG65FBO | LG65FBP | 0.857
LG65FBO | FE16RBX | 0.285
LG65FBO | LTZ1077 | 0.143
FE16RBX | LTZ1077 | 0.143
LTZ1077 | LTZ107 | 0.923

## Slide 32: License Plate Recognition - Testing
BX66HHO
LTZ1077

## Slide 33: License Plate Recognition - Testing
--
--

## Slide 34: License Plate Recognition - Testing
5HUTTLE
18001

## Slide 35: License Plate Recognition - Matching
@@##@@@ or @@@####
@ Letter
# Number

## Slide 36: License Plate Recognition - Matching
@@##@@@ or @@@####
Max 100%
@ Letter
# Number
Chart: Percentage Correct
| Regex Enabled | Regex Disabled
Min | 35.71 | 22.22
Avg | 62.62 | 42.28
Max | 100 | 66.67

## Slide 37: Peer to Peer Network - Aim
Transmit detected plates to other peers
Work out average speed between peer locations
http://pressednumberplates.co.uk/wp-content/uploads/2016/06/Pressed-Number-Plates.jpg

## Slide 38: Peer to Peer Network - Aim
http://pressednumberplates.co.uk/wp-content/uploads/2016/06/Pressed-Number-Plates.jpg

## Slide 39: Peer to Peer Network - Server
GET
POST
PATCH
DELETE
RESTful API
Run on top of a web server
Can be used for the web interface too

## Slide 40: Peer to Peer Network - Server
GET
POST
PATCH
DELETE

## Slide 41: Peer to Peer Network - Server
GET
POST
PATCH
DELETE
encryption
authentication
ID: fbbb1cbf-7887-4cc6-9bbf-16707e11367e
ID: 4feb662e-f50a-4088-bafe-ce75b421d50c
ID: 01ed4cfa-6c5b-476f-a6f8-4c6d0bcd5975

## Slide 42: Peer to Peer Network - Server
API
Unique ID authentication
Local encryption
GET
POST
PATCH
DELETE
encryption
authentication
ID: fbbb1cbf-7887-4cc6-9bbf-16707e11367e
ID: 4feb662e-f50a-4088-bafe-ce75b421d50c
ID: 01ed4cfa-6c5b-476f-a6f8-4c6d0bcd5975

## Slide 43: Peer to Peer Network - Design
Overkill for transferring text
Risky considering project timescale
Program security protection manually
http://cs.berry.edu/~nhamid/p2p/diagram1.jpg
https://www.researchgate.net/profile/Houssain_Kettani/publication/241972547/figure/fig1/AS:298617555439620@1448207381487/Figure-2-Classical-BitTorrent-P2P-Protocol-Sequence.png
http://www.umkc.edu/is/security/images/P2P_Explanation/gnutellaProtocol.gif
https://www-zeuthen.desy.de/technisches_seminar/texte/flink_se/img008.jpg

## Slide 44: Peer to Peer Network - Design
Tried, tested, scalable framework
Most security issues taken care of

## Slide 45: Peer to Peer Network - Trust System
Chart: Trust Decay (0.99)

## Slide 46: Peer to Peer Network - Trust System
Chart: Trust Decay (0.99)

## Slide 47: Peer to Peer Network - Trust System
Reward genuine, matching plates
Prevent fake plates
Prevent leeching
Chart: Trust Decay (0.99)

## Slide 48: Peer to Peer Network – Network Transactions
Bootstrap the network
Maintain the network
Security issues
Adapted from https://en.wikipedia.org/wiki/Peer-to-Peer_Protocol_(P2PP)
Register
Get list of peers
Keep alive
Send plates
Detect violations
Modify trust of peer

## Slide 49: Web Interface - Aim
What the user sees
Dashboard to control network
Post detected violations on social networks

## Slide 51
Agenda

## Slide 53: Demo
Modifications
Pre-recorded video
Live motion detection unused

## Slide 54: Demo
Modifications
Pre-recorded video
Live motion detection unused

## Slide 56
Agenda

## Slide 58: Evaluation
Implement a number plate recognition system using existing computer vision algorithms on a low-cost, readily available hardware platform.
Set up a peer-to-peer network to share vehicle passing times and detect violations without the need for a central server*.
Publish photo evidence of any violations
*) Except when bootstrapping
All main deliverables achieved

## Slide 59: Evaluation
Use the changes in the number plate geometry as the vehicle passes to detect the instantaneous speed of a vehicle
Implement automatic peer discovery
Add an encryption layer
Package the system so that it can be easily installed in a home by an inexperienced user.
All but 1 advanced deliverable achieved

## Slide 60: Conclusion
Challenging project
Very open ended on implementation
Usable immediately
Revisit performance and night time issues with LPR
Consider refactoring P2P to be standalone
Scalability testing
Attempt overnight test

## Slide 61: Thank you
http://github.com/jeremych1000/ee4-FYP/
©2017 Jeremy Chan. All rights reserved. | Powered by Django and OpenALPR | Created with love from the United Kingdom