## Slide 1: Distributed Road Traffic Speed Monitoring
Jeremy Chan
w/ Dr. Ed Stott
w/ Dr. Christos Papavassiliou
An EE4-T Final Year Project
Notes: Good morning.
My name is Jeremy Chan, and welcome to my final year project presentation, on creating a distributed road traffic speed monitoring system.

## Slide 2: At a glance…
Implementation based project
Catch speeding motorists using a camera and Raspberry Pi
Existing license plate recognition (LPR) technologies
New peer to peer network (P2P)
No government controlled central server
Social posting
Motivation / Specification / High Level Design /
Implementation and Testing / Demo / Evaluation and Conclusion
Notes: At a glance, this project is an implementation based project.
It uses a camera connected to a Raspberry Pi to catch speeding motorists by detecting their license plates, sharing it with others, and working out the average speed of the vehicle.
Details of speeding motorists can then be posted online on social platforms.
It leverages existing LPR technologies, but creates a NEW P2P network, eliminating the need for a central, government controlled, server
The rundown on this presentation is a general overview on the project details, followed by high level design of the individual components, followed by implementation and testing.
Finally, a demo, followed by an evaluation and a conclusion.

## Slide 3: Motivation - Accident areas
Chart: Casualties by severity and road type (2015)
| Fatal | Serious | Slight | All
Built Up | 43 | 67 | 73 | 72
Non Built Up | 51 | 30 | 22 | 23
Motorway | 6 | 3 | 5 | 5
95% of accidents not on motorway
Target residential areas
73%
72%
67%
43%
23%
22%
30%
51%
Built up
Non built up
Motorway
https://www.gov.uk/government/uploads/system/uploads/attachment_data/file/533293/rrcgb-main-results-2015.pdf
Notes: The main motivation of the project comes from reducing casualties from speeding cars.
While the higher the speed, the higher the fatality rate, most of the casualties lie in residential and urban areas.
Therefore, the system is targeted at providing average speed checks across non-motorway areas.

## Slide 4: Motivation - Fixed point speed cameras
https://a1.muscache.com/locations/uploads/photo/image/22901/0_4200_0_2800_one_westside-los-angeles-quiet-residential-street-devon0289.jpg
Notes: Regular average speed check cameras in all their yellow and orange glory are horrible to look at.
Putting a lot of them near homes would be detrimental to the streetscape, and therefore a discreet implementation is desired.

## Slide 5: Motivation - Fixed point speed cameras
https://a1.muscache.com/locations/uploads/photo/image/22901/0_4200_0_2800_one_westside-los-angeles-quiet-residential-street-devon0289.jpg

## Slide 6: Motivation - Fixed point speed cameras
Detrimental to streetscape
Prefer discreet appearance
Only take speed at a point
https://a1.muscache.com/locations/uploads/photo/image/22901/0_4200_0_2800_one_westside-los-angeles-quiet-residential-street-devon0289.jpg
Notes: Regular average speed check cameras in all their yellow and orange glory are horrible to look at.
Putting a lot of them near homes would be detrimental to the streetscape, and therefore a discreet implementation is desired.

## Slide 7: Motivation - Average speed cameras
http://www.trents.co.uk/wp-content/uploads/2014/12/Average-speed-camera.jpg
https://ichef-1.bbci.co.uk/news/660/cpsprodpb/0202/production/_89841500_033220635-2.jpg
None on residential routes
Notes: There are some license plate cameras on the market with different features like enhanced night time operation with superior digital signal processing.
However they are rather expensive and always use a central server to store the detected license plates.

## Slide 8: Motivation - Existing license plate cameras
https://www.bhphotovideo.com/images/images1000x1000/bosch_f_01u_245_613_dinion_capture_5000_license_1163861.jpg
https://www.securitycameraking.com/securityinfo/wp-content/uploads/2013/01/License-Plate-Capture-Camera-vs-License-Plate-Recognition-Camera-21-300x300.gif
Hard to buy for general public
>£ 1000
Proprietary storage of plates
Notes: There are some license plate cameras on the market with different features like enhanced night time operation with superior digital signal processing.
However they are rather expensive and always use a central server to store the detected license plates.

## Slide 9: Motivation - Summary
New system should:
Target general public
Priced reasonably
Not aim to directly ticket offender
Use as evidence and leverage for demands
Notes: There are some license plate cameras on the market with different features like enhanced night time operation with superior digital signal processing.
However they are rather expensive and always use a central server to store the detected license plates.

## Slide 10: Product Specification - Main Deliverables
Implement a UK number plate recognition system using existing computer vision algorithms on a low-cost, readily available hardware platform.
Set up a peer-to-peer network to share vehicle passing times and detect violations without the need for a central server.
Publish photo evidence of any violations
Notes: Therefore, the main deliverables of the project were formulated as follows:
The system should leverage existing computer vision algorithms to provide license plate recognition capabilities
For sake of simplicity, no custom plates, and only UK format
A peer to peer network should be created to share the detected plates with no need for a central server
The license plates should be able to be published online for further police action

## Slide 11: Product Specification - Main Deliverables
Implement a UK number plate recognition system using existing computer vision algorithms on a low-cost, readily available hardware platform.
Set up a peer-to-peer network to share vehicle passing times and detect violations without the need for a central server.
Publish photo evidence of any violations
Notes: Therefore, the main deliverables of the project were formulated as follows:
The system should leverage existing computer vision algorithms to provide license plate recognition capabilities
For sake of simplicity, no custom plates, and only UK format
A peer to peer network should be created to share the detected plates with no need for a central server
The license plates should be able to be published online for further police action

## Slide 12: Product Specification - Main Deliverables
Implement a UK number plate recognition system using existing computer vision algorithms on a low-cost, readily available hardware platform.
Set up a peer-to-peer network to share vehicle passing times and detect violations without the need for a central server.
Publish photo evidence of any violations
Notes: Therefore, the main deliverables of the project were formulated as follows:
The system should leverage existing computer vision algorithms to provide license plate recognition capabilities
For sake of simplicity, no custom plates, and only UK format
A peer to peer network should be created to share the detected plates with no need for a central server
The license plates should be able to be published online for further police action

## Slide 13: Product Specification - Main Deliverables
Implement a UK number plate recognition system using existing computer vision algorithms on a low-cost, readily available hardware platform.
Set up a peer-to-peer network to share vehicle passing times and detect violations without the need for a central server.
Publish photo evidence of any violations
Notes: Therefore, the main deliverables of the project were formulated as follows:
The system should leverage existing computer vision algorithms to provide license plate recognition capabilities
For sake of simplicity, no custom plates, and only UK format
A peer to peer network should be created to share the detected plates with no need for a central server
The license plates should be able to be published online for further police action

## Slide 14: Product Specification - Advanced Deliverables
Have a standalone mode in case there is no one in the network
Be able to join/leave/return to the network easily
Make the network secure against rogue peers
Package the system so that it can be easily installed in a home by an inexperienced user

## Slide 15: Product Specification - Advanced Deliverables
Have a standalone mode in case there is no one in the network
Be able to join/leave/return to the network easily
Make the network secure against rogue peers
Package the system so that it can be easily installed in a home by an inexperienced user

## Slide 16: Product Specification - Advanced Deliverables
Have a standalone mode in case there is no one in the network
Be able to join/leave/return to the network easily
Make the network secure against rogue peers
Package the system so that it can be easily installed in a home by an inexperienced user

## Slide 17: Product Specification - Advanced Deliverables
Have a standalone mode in case there is no one in the network
Be able to join/leave/return to the network easily
Make the network secure against rogue peers
Package the system so that it can be easily installed in a home by an inexperienced user

## Slide 18: Product Specification - Advanced Deliverables
Have a standalone mode in case there is no one in the network
Be able to join/leave/return to the network easily
Make the network secure against rogue peers
Package the system so that it can be easily installed in a home by an inexperienced user

## Slide 19: Envisioned System
(1) 9:41 pm
(1) 9:41 pm
(1) 9:41 pm
(2) 9:44 pm
(2) 9:44 pm
(2) 9:44 pm
Yellow – locally detected
White – peer detected
1
2
3

## Slide 20: High Level Design
3 well defined modules
Readily available components
Users have control over data
License Plate Detection
Peer to Peer Network
Web Interface

## Slide 21: License Plate Recognition - Aim
Get license plates of cars
Function in multiple angles and lighting conditions

## Slide 22: License Plate Recognition - Design
Store videos locally using motion detection
Detect license plates using OpenALPR
Extract unique plates
Multiple parameters for tweaking
Store plates with metadata in database
Consecutive frames will likely be the same car
Process videos when idle
  Time
  Location
OpenALPR computationally expensive
Buffer videos
Survive busy periods and power outages

## Slide 23: License Plate Recognition - Fuzzy Grouping
<<<<<1< LG65FBO <2< LG65FBP <3< LG65FBO <4< FE16RBX <5< LTZ1077 <6< LTZ077 <7< LTZ107
 | Plate1 | Plate 2 | String Similarity (0.75)
1-2 | LG65FBO | LG65FBP | 0.857
2-3 | LG65FBP | LG65FBO | 0.857
3-4 | LG65FBO | FE16RBX | 0.285
4-5 | FE16RBX | LTZ1077 | 0.143
5-6 | LTZ1077 | LTZ077 | 0.923
6-7 | LTZ077 | LTZ107 | 0.857
Robust separation of unique vehicles
Works with misreads
Sort groups by confidence

## Slide 24: License Plate Recognition - Fuzzy Grouping
Robust separation of unique vehicles
Works with misreads
Sort groups by confidence
<<<<<1< LG65FBO <2< LG65FBP <3< LG65FBO <4< FE16RBX <5< LTZ1077 <6< LTZ077 <7< LTZ107
 | Plate1 | Plate 2 | String Similarity (0.75)
1-2 | LG65FBO | LG65FBP | 0.857
2-3 | LG65FBP | LG65FBO | 0.857
3-4 | LG65FBO | FE16RBX | 0.285
4-5 | FE16RBX | LTZ1077 | 0.143
5-6 | LTZ1077 | LTZ077 | 0.923
6-7 | LTZ077 | LTZ107 | 0.857

## Slide 25: License Plate Recognition - Testing
LF64FBO
LM55BCK

## Slide 26: License Plate Recognition - Testing
BX66HHO
LTZ1077

## Slide 27: License Plate Recognition - Testing
--
--

## Slide 28: License Plate Recognition - Testing
5HUTTLE
18001

## Slide 29: License Plate Recognition - Matching
@@##@@@ or @@@####
@ Letter
# Number

## Slide 30: License Plate Recognition - Matching
@@##@@@ or @@@####
LPR output compared with manual
Max 100%
@ Letter
# Number
Chart: Automated Test Suite of 20 videos
| Regex Enabled | Regex Disabled
Min | 35.71 | 22.22
Avg | 62.62 | 42.28
Max | 100 | 66.67

## Slide 31: False positive slide

## Slide 32: Peer to Peer Network - Aim
Transmit detected plates to other peers
Work out average speed between peer locations
http://pressednumberplates.co.uk/wp-content/uploads/2016/06/Pressed-Number-Plates.jpg

## Slide 33: Peer to Peer Network – Network Transactions
Bootstrap the network
Maintain the network
Security issues
Adapted from https://en.wikipedia.org/wiki/Peer-to-Peer_Protocol_(P2PP)
Register*
Get list of peers
Keep alive
Send plates
Detect violations
Modify trust of peer
*) Requires central server

## Slide 34: Peer to Peer Network - Aim
http://pressednumberplates.co.uk/wp-content/uploads/2016/06/Pressed-Number-Plates.jpg

## Slide 35: Peer to Peer Network - Aim
http://pressednumberplates.co.uk/wp-content/uploads/2016/06/Pressed-Number-Plates.jpg

## Slide 36: Peer to Peer Network - Server
P2P on top of web server
API
Unique ID authentication
Local encryption
GET
POST
PATCH
DELETE
encryption
authentication
ID: fbbb1cbf-7887-4cc6-9bbf-16707e11367e
ID: 4feb662e-f50a-4088-bafe-ce75b421d50c
ID: 01ed4cfa-6c5b-476f-a6f8-4c6d0bcd5975

## Slide 37: Peer to Peer Network - Design
Tried, tested, scalable framework
Most security issues taken care of

## Slide 38: Peer to Peer Network - Trust System
Chart: Trust Decay (0.99)
Self | Peer (1min)
LK14VJV | 
LX04CZT | 
RF66BEU | 
KN14BVY | 
SH14PVZ | 
LL12EFH | 

## Slide 39: Peer to Peer Network - Trust System
Chart: Trust Decay (0.99)
Self | Peer (1min)
LK14VJV | LK14VJV
LX04CZT | LX04CZT
RF66BEU | RF66BEU
KN14BVY | KN14BVY
SH14PVZ | SH14PVZ
LL12EFH | LL12EFH

## Slide 40: Peer to Peer Network - Trust System
Chart: Trust Decay (0.99)
Self | Peer (10min)
LK14VJV | LK14VJV
LX04CZT | 
RF66BEU | RF66BEU
KN14BVY | KN14BVY
SH14PVZ | 
LL12EFH | 

## Slide 41: Peer to Peer Network - Trust System
Chart: Trust Decay (0.99)
Self | Rogue Peer
LK14VJV | HI MOM
LX04CZT | !@$%^&**
RF66BEU | FAKE_FAKE
KN14BVY | AAAAAAA
SH14PVZ | 
LL12EFH | 

## Slide 42: Peer to Peer Network - Trust System
Chart: Trust Decay (0.99)
Ignore rogue
Reward genuine, matching plates
Prevent fake plates
Prevent leeching

## Slide 43: Web Interface - Aim
What the user sees
Dashboard to control network
Post detected violations on social networks

## Slide 44: Demo
Modifications
Pre-recorded video
Live motion detection unused

## Slide 45: Evaluation
Implement a number plate recognition system using existing computer vision algorithms on a low-cost, readily available hardware platform.
Set up a peer-to-peer network to share vehicle passing times and detect violations without the need for a central server*.
Publish photo evidence of any violations
*) Except when bootstrapping
All main deliverables achieved

## Slide 46: Evaluation
All but 1 advanced deliverable achieved
Have a standalone mode in case there is no one in the network
Be able to join/leave/return to the network easily
Make the network secure against rogue peers
Package the system so that it can be easily installed in a home by an inexperienced user

## Slide 47: Conclusion
Challenging project
Very open ended on implementation
Usable immediately
Revisit performance and night time issues with LPR
Consider refactoring P2P to be standalone
Scalability testing
Attempt overnight test

## Slide 48: Thank you
http://github.com/jeremych1000/ee4-FYP/
©2017 Jeremy Chan. All rights reserved. | Powered by Django and OpenALPR | Created with love from the United Kingdom